## Slide 1: How to design a CPU?

## Slide 2: Content
Computer Architecture Fundamentals
How does a CPU work?
Single Cycle CPU Datapath
Single Cycle CPU Design Process
Run simulation on Vivado

## Slide 3: Computer Architecture Fundamentals
MIPS Architecture

## Slide 4: Computer Architecture Fundamentals
Sequencing
Selection
Iteration

## Slide 5: How does a CPU work?
Instruction Fetch
Instruction Decode
Execute
Memory Access
Register Write

## Slide 6: Instruction Fetch
Fetch the Instruction
Update PC (Program Counter)
  Sequential:
    PC <= PC + 4
  Branch/Jump:
    PC <= something else
Address
Instruction Memory
PC
Next Address Logic
Instruction Word
32

## Slide 7: Instruction Decode
Sending the fetched instruction’s opcode and function field bits to the Control Unit
For R-type: read 2 registers
For I-type: read 1 register and sign-extent the immediate
For J-type: just jump

## Slide 8: Execute
Run the operations
  Add
  Sub
  And
  Or
  If A-B = 0, Zero <= 1
  Nor
  Xor
  Shift
  Comparisons

## Slide 9: Memory Access
Instructions except load and store do nothing during this stage.
For load
  Read values from Data Memory
For store
  Write values into Data Memory

## Slide 10: Register Write
Write the result back into the corresponding register

## Slide 11: Data Path

## Slide 12: Single Cycle CPU Design Process
Software: Xilinx Vivado
Programing language: Verilog HDL

## Slide 13: Instruction Memory

## Slide 14: Register File
input | clk
input | reset
input | RsAddr[4:0]
input | RtAddr[4:0]
input | regWriteData[31:0]
input | regWriteAddr[4:0]
input | regWriteEn
output | RsData[31:0]
output | RtData[31:0]

## Slide 15: Control Unit
input | opcode[5:0]
input | funct[5:0]
output | reg_dst
output | imm_expand
output | alu_srcA
output | alu_srcB[1:0]
output | memtoreg
output | regwrite
output | memread
output | memwrite
output | aluop[2:0]
output | jmp
output | jal
output | jr
output | branch
output | bne
output | bgtz
output | bltz
output | lui

## Slide 16
控制信号名 | 0 | 1
reg_dst | 写寄存器组寄存器的地址，来自rt字段 | 写寄存器组寄存器的地址，来自rd字段
imm_expand | (sign-extend)immediate（符号扩展） | (zero-extend)immediate（0扩展）
alu_srcA | 来自寄存器堆 RsData 输出 | 来自寄存器堆 RtData 输出，相关指令
memtoreg | 来自ALU运算结果(aluRes)的输出 | 来自数据存储器（Data Memory）的输出
memwrite | 无操作 | 写数据存储器（Data Memory）
memread | 输出高阻态（z） | 读数据存储器（Data Memory）
regwrite | 无操作 | 写指令存储器（Instruction Memory）
jmp | 无操作 | 跳转至{add4[31:28], inst[25:0], 2'b00}
jal | 无操作 | 将PC+4的地址写入寄存器$31（$ra）
jr | 无操作 | 跳转至寄存器中所存储的地址
branch | 无操作 | 跳转至pc+4+(sign-extend)immediate<<2（zero=0）
bne | 无操作 | 跳转至pc+4+(sign-extend)immediate<<2（zero≠0）
bgtz | 无操作 | 若RsData>0则跳转至pc+4+(sign-extend)immediate<<2
bltz | 无操作 | 若RsData<0则跳转至pc+4+(sign-extend)immediate<<2
lui | 无操作 | 将16位立即数放到目的寄存器高16位，寄存器的低16位填0
alu_srcB[1:0] | 00：RtData 01：(extend)immediate 10：{27'b000000000000000000000000000,inst[10:6]} 11：RsData | 
aluop[2:0] | 具体见表2 ALU 运算功能表 | 

## Slide 17: ALUCtr
input | ALUOp[2:0]
input | funct[5:0]
output | ALUCtr[3:0]

## Slide 18
aluop[2:0] | funct[5:0] | aluCtr[3:0] | 功能描述
010/111 | xxxxxx/100100 | 0000 | 与
011/111 | xxxxxx/100101 | 0001 | 或
000/111 | xxxxxx/10000x | 0010 | 加
100/111 | xxxxxx/100110 | 0100 | 异或
111 | 100111 | 0101 | 或非
001/111 | xxxxxx/10001x | 0110 | 减
101/111 | xxxxxx/101010 | 0111 | 小于设置（有符号数）
111 | 000x00 | 1000 | 逻辑左移
111 | 000x10 | 1001 | 逻辑右移
111 | 000x11 | 1010 | 算数右移
110/111 | xxxxxx/101011 | 1101 | 小于设置（无符号数）
ALU运算功能表

## Slide 19: ALU
input | input1[31:0]
input | input2[31:0]
input | lui
output | alures[31:0]
output | zero

## Slide 20: Signext
input | inst[15:0]
input | imm_expand
output | data[31:0]

## Slide 21: Data Memory
input | clk
input | reset
input | addra
input | dina
input | rea
input | wea
output | douta

## Slide 22: Run simulation on Vivado
addiu $1, $0, 8 slt $7, $6, $1

## Slide 23: Run simulation on Vivado
bne $8, $1, -2

## Slide 24: Run simulation on Vivado
j 0x00000058